## Slide 1
Correct composition via isolation
Behavior of an extension must not change when composed with others
Custom instructions only access registers & selected CFU’s state context
  Each interface/CFU may have 0, 1, #harts, or n isolated state contexts
HW-SW interface: custom interface multiplexing
Inexhaustible, collision-free instruction encodings
mcfu_selector CSR selects hart’s current CFU and some state context
custom-0/-1/-2 functions routed to the selected CFU
CFU performs function, may update its state context
CFU response updates destination register and cfu_status CSR
Example accelerated library programming model
Try to select a custom interface, issue custom instructions if CFU present
  CI bitmanip(CI_ID_IBitmanip); // csrrw mcfu_selector …
  if (bitmanip) // accelerator present: count = cf(pcnt_cf, data, 0); // cfu_reg pcnt_cf,rd,data,x0 else // accelerator not present: count = popcount(data); // software version
HW-HW interface: CFU Logic Interface (CFU-LI)
Flexible feature levels: combinational, fixed, variable latency, reordering
Prebuilt switches & adapters for glueless composition
Example: CFU-L2 variable latency signaling:
Learn more
Draft Proposed RISC-V Composable Custom Extensions Specification, https://github.com/grayresearch/CFU
Status: refining spec, building CPUs+CFUs composition demos
Join us! Discuss, meet on RISC-V [sig-soft-cpu] list
Composable Custom Extensions and Custom Function Units for RISC-V
Jan Gray (Gray Research) , Tim Vogt (Lattice Semiconductor), Tim Callahan (Google), Charles Papon (SpinalHDL),
Guy Lemieux (University of British Columbia), Maciej Kurc (Antmicro), Karol Gugala (Antmicro), Olof Kindgren (Qamcom)
RISC-V custom extensions’ interop problem
Standard extensions layer and compose well. Each takes years to ratify
Custom extensions allow rapid in-house accelerator & library solutions
  Solutions may not work together – conflicting encodings, different means of discovery, computation, state, error handling, versioning
  Incompatible solution silos limit reuse and fragment the ecosystem
Let us build a mix-and-match custom extensions future
Agility of custom extensions with composability of standard extensions
Proposed HW-SW and HW-HW interop interfaces enable reusable accelerators that just work together – a marketplace of accelerators
Key ideas
Custom interface (CI): abstracts a composable custom extension
Custom function unit (CFU): core that implements a custom interface
Accelerated library: issues custom instructions of a custom interface
New interop interfaces
HW-SW: interface multiplexing: libs select hart’s current CI & CI-state → each custom interface enjoys full custom instruction encoding space
HW-HW: CFU Logic Interface (CFU-LI): CFU signaling standard → automatic composition of CPU+CFU complexes
Example
HW-SW stack changes
Custom Interface Runtime: accelerated library services (discovery …)
“-Zicfu”: interface multiplexing CSRs: mcfu_select, cfu_status
CFU Logic Interface & metadata: automatic CPUs+CFUs composition
Some composition challenges we address
Dynamic discovery of custom extensions
Namespace / ID management with no central authority
Collision free custom instruction encodings
Correct composition of stateful custom extensions
Uniform error handling
Uniform context save/restore
Versioning of custom extensions
Privileged systems: access control to extensions and state
Please see spec for all the details
id status data
cfu_reg cf_id rd rs1 rs2
datapath
register file
cfu_id state_id en=1
cu op fi of si ci
instruction
mcfu_selector
cfu_status
request
CFUs
CPU
response
state contexts
id cfu state insn func data0 data1
ALU
Accelerated Application (Composed Software)
Accelerated System (Composed Hardware)
CPU0 <2>
CPU1 <2>
Switch
Cryptography CFU <4>
Compression CFU <4>
bobs_bnn_cfu <4>
Crypt. library
Comp. library
ML library
Runtime
System CFU map
CPU MD
Mux MD
Crypt. MD
CPU RTL
Mux RTL
Crypt. CFU RTL
Comp. MD
bobs_bnn_cfu MD
Comp. CFU RTL
bobs_bnn_ cfu RTL
System manifest
Composer
Composable CPU and CFU Packages
RV-I -Zicsr
-Zicfu
CFU Logic Interface
CI-ABI
CPU
CFU0
CFU1
CI-RT
CI0
CI1
CFU Metadata
CFU0-MD
CFU1-MD
CI0 lib
CI1 lib
SYS-MD
CPU-MD
Applications
Language-VM / OS / VM
-uses

mcfu_selector CSR cfu_status CSR
cfu reg cf_id,rd,rs1,rs2 cfu_imm cf_id,rd,rs1,imm cfu_flex cf_id,rs1,rs2
Let’s define a common custom extensions architecture so our custom extensions “just work” together